## Slide 1: Introduction to 8086 Microprocessor
Presented by
Mahbubur Rahman
Lecturer
Department of Computer Science and Engineering(CSE)
Green University of Bangladesh(GUB)

## Slide 2: Outline
Introduction to 8086 Microprocessor
Features of 8086
Comparison between 8085 and 8086 Microprocessor
Flag Registers in 8086
02

## Slide 3: Introduction to 8086 Microprocessor
8086 Microprocessor is an enhanced version of 8085 Microprocessor.
It is a 16-bit Microprocessor. (which means it has 16 bit data bus)
8086 has a 20-bit address bus can access upto 220 (1 MB) memory locations.
It can support upto 64K I/O ports.
It provides 14, 16-bit registers.
It consists of powerful instruction set, which provides operations like multiplication and division easily.
It supports two modes of operations, i.e. Maximum mode and Minimum mode. Maximum mode is suitable for system having multiple processors and Minimum mode is suitable for system having single processor.
03

## Slide 4: Features of 8086 (1/2)
It has an instruction queue , which is capable of storing 6 instruction bytes from the memory resulting in faster processing.
It was the first 16-bit processor having 16-bit ALU, 16-bit registers, internal data bus, and 16-bit external data bus.
It is available in 3 versions based on the frequency of operation
  8086: 5 MHz
  8086-2: 8 MHz
  (c) 8086-1: 10 MHz
04

## Slide 5: Features of 8086 (2/2)
It has 256 vectored interrupts.
It requires +5V power supply.
A 40-pin dual in line package.
It uses two stages of pipelining, i.e. Fetch Stage and Execute Stage, which improves performance.
It has multiplexed address and data bus AD0 – AD15 and A16 – A19.
It requires single phase clock with 33% duty cycle to provide internal timing.
Duty cycle is the ratio of time a load or circuit is ON compared to the time the load or circuit is OFF.
05

## Slide 6: Comparison between 8085 and 8086
Size: 8085 is 8-bit Microprocessor, whereas 8086 is 16-bit Microprocessor.
Address bus: 8085 has 16-bit address bus while 8086 has 20-bit address bus.
Memory: 8085 can access up to 64 KB, 8086 can access up to 1 MB of memory.
Instruction queue: 8085 doesn’t have an instruction queue, whereas 8086 has an instruction queue.
Pipelining: 8085 doesn’t support a pipelined architecture while 8086 supports a pipelined architecture.
I/O: 8085 can access 28 = 256 I/O’s, whereas 8086 can access 216 = 64k I/O’s.
Cost: The cost of 8085 is low whereas that of 8086 is high.
06

## Slide 7: Flag Registers in 8086
8086 Microprocessor has 16-bit flag register. ( 9 flags are there and 7 bits unused)
Among 9 flags we divided into 2 categories: 6 Status flags and 3 control flags.
6 status flag are carry flag, auxiliary carry flag, zero flag, sign flag, parity flag and overflow flag.
3 control flags are direction flag, Interrupt Enable flag and Trap flag.
07

## Slide 8: Flag Registers in 8086
Trap flag: TF=0, the processor will enter in single step execution mode.
Interrupt flag: IF=0, maskable interrupts are recognized.
Direction flag: Used for string manipulation instruction.
If DF=0, Auto increment mode, DF=1, Auto decrement mode.
Overflow flag: OF=1, if the result is too large positive number or too small negative number to fit in accumulator. (-12810 to 12710)
08

## Slide 9: Flag Registers in 8086
Example: If Register AL = 7Fh and the instruction ADD AL,1 is executed. How the flag values will change in 8086 microprocessor?
AL = 80h = 12810 = (1000 0000)2
CF = 0, there is no carry
PF = 0, 80h has odd number of ones
AF = 1, there is a carry out of bit 3 into bit 4
ZF = 0, result is not zero
SF = 1, msb is one
OF = 1, output is greater than 12710
09

## Slide 10: Internal Architecture of 8086
Divided into two independent functional units.
Bus Interface Unit
  Instruction Pointer (IP)
  Instruction Queue
  Segment Register
Execution Unit
Pointer and Indexed Register: 8086 has two pointers and two indexed registers. Stack Pointer (SP), Base Pointer (BP), Source Index (SI) and Destination Index (DI).
10

## Slide 11: Segment Register
The memory space 1MB of 8086 is segment into 4 blocks. Each block specified by register with maximum size 64KB.
Code segment (CS)
Data segment (DS)
Stack segment (SS)
Extra segment (ES)
11

## Slide 12: Memory Segmentation
8086 has 20 lines address bus but 16 lines data bus.
We store 20 bits address using 16 bit address registers.
Example: DS = 2222h and offset = 0016h.
Logical address: 2222h:0016h ( Segment : Offset)
Physical address: 2222h*10 + 0016h = 22220h + 0016h
12

## Slide 13: Segment Registers with offset
Code segment (CS) with IP
Data segment (DS) with BX,DI,SI
Extra segment (ES) with DI
Stack segment (SS) with SP, BP
13

## Slide 14: Memory Segmentation
Example 02: PA = 13BB5h and offset = 1235h. Calculate segment address of ES
PA = ES * 10 + Offset
ES = (PA - offset) / 10 = 1298h
14

## Slide 15: Memory Segmentation
Example 03: SS = 3864h, SP = 1735h, BP = 4826h
The address calculated when BP is taken as the offset gives the starting address of stack.
When SP is taken as offset denotes the memory location where the top of the stack is.
14

## Slide 16: Thank You
40