## Slide 1: Instruction Set of 8085 Microprocessor
Presented by
Mahbubur Rahman
Lecturer
Department of Computer Science and Engineering(CSE)
Green University of Bangladesh(GUB)

## Slide 2: Instruction Set of 8085 Microprocessor

## Slide 3
Instruction Set of 8085 Microprocessor
  An instruction is a binary pattern designed inside a microprocessor to perform a specific function.
  The entire group of instructions that a microprocessor supports is called Instruction Set.
  8085 has 246 instructions.
  Each instruction is represented by an 8-bit binary value.
  These 8-bits of binary value is called Op-Code or Instruction Byte.

## Slide 4
An instruction is a command given to the microprocessor to perform a specific operation on data.
Basically there are five groups of instructions –
  Data transfer instructions – these instructions are used to transfer the data from one register to another register or memory to register etc.
  Arithmetic instructions – these instructions are going to perform arithmetic operations like addition, subtraction etc.
  Logical instructions – these instructions are going to perform logical operations like AND, OR, XOR etc.
  Branching instructions – these instructions are going to design inside the program controller where we need to jump the program control. Example: JUMP, CALL, RETURN etc.
  I/O and Machine control instructions – these instruction contains I/O and machine related contents.

## Slide 5
Data Transfer Instructions:
These are used for data transfer from one place to another place.
Instruction | Operation
MOV R1, R2 | R1 R2
MOV M, R (M points to HL register pair) | M R
MOV R, M | R M
MVI R, FFH | R FFH
MVI R, 8-bit data | R 8-bit data
LXI SP, 8-bit data | SP 8-bit data

## Slide 6
Arithmetic Instructions
Instruction | Operation | Instruction | Operation | Instruction | Operation
ADD R | A A+R | ADC R | A A+R+CY | INR R | R R+1
ADD M | A A+M | ADC M | A A+M+CY | INR M | M M+1
ADI 8-bit data | A A+8-bit data | ADC 8-bit data | A A+8-bit data+CY | DCR R | R R-1
SUB R | A A-R | SBB R | A A-R-CY | DCR M | M M-1
SUB M | A A-M | SBB M | A A-M-CY | INX rp | rp rp+1
SUI 8-bit data | A A-8 bit data | SBI 8-bit data | A A-8-bit data-CY | DCX rp | rp rp-1

## Slide 7
Logical Instructions
Instruction | Operation | Instruction | Operation | Instruction | Operation
ANA R | A AɅR | XRA R | A A⊕R | RLC | Rotate Left without carry
ANA M | A AɅM | XRA M | A A⊕M | RRC | Rotate Right without carry
ANI 8-bit data | A AɅ8-bit data | XRA 8-bit data | A A⊕8-bit data | RAL | Rotate Left with carry
ORA R | A AVR | CMP R | A A-R | RAR | Rotate Left with carry
ORA M | A AVM | CMP M | A A-M | CMA | Complement Accumulator
ORI 8-bit data | A AV8-bit data | CPI 8-bit data | A A-8-bit data | CMC | Complement Carry

## Slide 8
Branching Instructions
We are having three types of branching instructions.
  Jump (Unconditional and Conditional) – Example: JUMP 16 bit address
  Call (Unconditional and Conditional) – Example: CALL 16 bit address (PUSH)
  Return (Unconditional and Conditional) – Example: RET (POP)
  Condition depends on flag registers.
  NZ (Z=0), Z (Z=1) C (C=1) NC (C=0) PE (P=1) PO (P=0) P(Plus) (S=0) M (Minus) (S=1)
  In every JUMP instruction Program counter (PC) is going to catch the 16 bit address
  Ex: JNZ, JZ, JC, JNC, JPE, JPO, JP, JM
  In every CALL instruction Stack Pointer (SP) is decremented by 2
  Ex: CNZ, CZ, CC, CNC, CPE, CPO, CP, CM
  In every RET instruction Stack Pointer (SP) is incremented by 2
  Ex: RNZ, RZ, RC, RNC, RPE, RPO, RP, RM

## Slide 9
Stack, I/O and Machine Control Instructions
This is the last category of instruction set in 8085 microprocessor which is having totally 10 instructions into 3 categories.
Stack: i. PUSH – Push two bytes of data into stack.
ii. POP – Pop two bytes of data from stack.
iii. HTHL – Exchange top of stack with HL.
iv. SPHL – Move contents of HL to stack.
I/O: v. IN – Initiate input operation. Example: IN 8 bit data A 8 bit data
vi. OUT – Initiate output operation. Example: OUT 8 bit data A 8 bit data
Machine Control: vii. EI – Enable interrupt All interrupts are enabled
viii. DI – Disable interrupt RST 7.5, 6.5, 5.5 and INTR will be disabled
ix. HLT – Microprocessor is halted
x. NoP – No operation