## Slide 1: Interrupt Vector Table
Presented by
Mahbubur Rahman
Lecturer
Department of Computer Science and Engineering(CSE)
Green University of Bangladesh(GUB)

## Slide 2
Interrupt Vector Table (IVT)
IVT is a structured list containing the addresses of Interrupt Service Routine (ISR) for various interrupts. It is also known as Interrupt Pointer Table (IPT).
INT N, N = Type Number = 0 to 255  256 Software Interrupts
IVT should have the addresses of ISR for 256 interrupts.
Physical Address = Code Segment and Instruction Pointer = CS X 10H + IP = 20 bits in size.
CS = 2 bytes and IP = 2 bytes.
So there is unique 256 interrupts ISR addresses.
256 interrupts = 256 X 4 = 1024 bytes = 1KB is located in the starting part of memory.
Address range will be CS : IP = 0000 : 0000 to 0000 : 03FFH

## Slide 3
Interrupt Vector Table (IVT)
CS : IP | Physical Address | Memory
0000 : 0000 | 00000 | 1 byte size
0000 : 0001 | 00001 | 1 byte size
0000 : 0002 | 00002 | 1 byte size
0000 : 0003 | 00003 | 1 byte size
0000 : 0004 | 00004 | 1 byte size
0000 : 0005 | 00005 | 1 byte size
0000 : 0006 | 00006 | 1 byte size
0000 : 0007 | 00007 | 1 byte size
0000 : 0008 | 00008 | 1 byte size
0000 : 0009 | 00009 | 1 byte size
0000 : 000A | 0000A | 1 byte size

## Slide 4
Interrupt Vector Table (IVT)
CS : IP | Physical Address | Memory
……… | ……… | ………
0000 : 03F6 | 003F6 | 1 byte size
0000 : 03F7 | 003F7 | 1 byte size
0000 : 03F8 | 003F8 | 1 byte size
0000 : 03F9 | 003F9 | 1 byte size
0000 : 03FA | 003FA | 1 byte size
0000 : 03FB | 003FB | 1 byte size
0000 : 03FC | 003FC | 1 byte size
0000 : 03FD | 003FD | 1 byte size
0000 : 03FE | 003FE | 1 byte size
0000 : 03FF | 003FF | 1 byte size

## Slide 5
For any interrupt to be pointed to an ISR we need 4 bytes.
Type number = 0 to 255
Type 0 interrupt (Divide by 0)
To execute Type 0 interrupt in needs to go to the specific ISR.
Higher memory address contains higher byte and lower memory address contains lower byte.
IP for the ISR of Type N = 4N (Where, N is Type number)
CS for the ISR of Type N = 4N+2 (Where, N is Type number)
For Type 1, IP = 4X1 = 00004H and CS = 4X1+2 = 00006H.

## Slide 6
CS : IP | Physical Address | Memory
0000 : 0000 | 00000 | IP (Lower byte) for Type 0
0000 : 0001 | 00001 | IP (Higher byte) for Type 0
0000 : 0002 | 00002 | CS (Lower byte) for Type 0
0000 : 0003 | 00003 | CS (Higher byte) for Type 0
0000 : 0004 | 00004 | IP (Lower byte) for Type 1
0000 : 0005 | 00005 | IP (Higher byte) for Type 1
0000 : 0006 | 00006 | CS (Lower byte) for Type 1
0000 : 0007 | 00007 | CS (Higher byte) for Type 1
0000 : 0008 | 00008 | ………
0000 : 0009 | 00009 | ………
0000 : 000A | 0000A | ………

## Slide 7
CS : IP | Physical Address | Memory
……… | ……… | ………
0000 : 03F6 | 003F6 | ………
0000 : 03F7 | 003F7 | ………
0000 : 03F8 | 003F8 | IP (Lower byte) for Type 254
0000 : 03F9 | 003F9 | IP (Higher byte) for Type 254
0000 : 03FA | 003FA | CS (Lower byte) for Type 254
0000 : 03FB | 003FB | CS (Higher byte) for Type 254
0000 : 03FC | 003FC | IP (Lower byte) for Type 255
0000 : 03FD | 003FD | IP (Higher byte) for Type 255
0000 : 03FE | 003FE | CS (Lower byte) for Type 255
0000 : 03FF | 003FF | CS (Higher byte) for Type 255

## Slide 8: Example: Determine the physical address of the ISR for the given IVT if Type 0 interrupt is encountered by 8086 microprocessor.
CS : IP | Physical Address | Memory
0000 : 0000 | 00000 | 05H
0000 : 0001 | 00001 | 34H
0000 : 0002 | 00002 | 00H
0000 : 0003 | 00003 | 20H
……… | ……… | ………
……… | ……… | ………
……… | ……… | ………
2000 : 3405 | 23405 | MOV AX, BX (in Hex Code)
2000 : 3406 | 23406 | ………
2000 : 3407 | 23407 | ………
2000 : 3408 | 23408 | ………

## Slide 9
Solution:
Type 0, N = 0
IP = 4N = 4X0 = 00000H (Address of the ISR IP)
IP is stored at this address. This is not the value of the IP, it is the value at which the IP of the ISR will be located.
CS = 4N+2 = 4X0+2 = 00002H (Address of the ISR CS)
IP of the ISR = 3405H
CS of the ISR = 2000H
Physical Address = CSX10H+IP = 2000X10+3405 = 23405H (Answer)

## Slide 10: Example: Determine the physical address of the ISR for the given IVT if Type 255 interrupt is encountered by 8086 microprocessor.
CS : IP | Physical Address | Memory
0000 : 0000 | 00000 | 05H
0000 : 0001 | 00001 | 34H
0000 : 0002 | 00002 | 00H
0000 : 0003 | 00003 | 20H
……… | ……… | ………
……… | ……… | ………
……… | ……… | ………
0000 : 03FC | 003FC | 22H
0000 : 03FD | 003FD | 33H
0000 : 03FE | 003FE | 00H
0000 : 03FF | 003FF | 40H

## Slide 11
Solution:
Type 255, N = 255
IP = 4N = 4X255 = 1020D = 003FCH (Address of the ISR IP)
IP is stored at this address. This is not the value of the IP, it is the value at which the IP of the ISR will be located.
CS = 4N+2 = 4X0+2 = 1022D = 003FEH (Address of the ISR CS)
IP of the ISR = 3322H
CS of the ISR = 4000H
Physical Address = CSX10H+IP = 3322X10+4000 = 43322H (Answer)

## Slide 12
Dedicated Interrupts (5) – Type 0 to Type 4 – They also called as predefined interrupts.
Reserved Interrupts (27) – Type 5 to Type 31 – Reserved by Intel for use in its future level of processors.
Available Interrupts (224) – Type 32 to Type 255 – Available to the user to be used as hardware or software interrupts.
Whether it is an external (h/w) or an internal (s/w) interrupt  mapped to Type number (N)

## Slide 13
The starting addresses of different types of interrupts are – (Range of different categories)
Interrupt Type | Starting Address | Interrupt Type | Starting Address
Type 0 | 00000H | Type 32 | 00080H
Type 1 | 00004H | Type 33 | 00084H
Type 2 | 00008H | Type 34 | 00088H
Type 3 | 0000CH | Type 35 | 0008CH
Type 4 | 00010H | ……… | ………
Type 5 | 00014H | ……… | ………
Type 6 | 00018H | ……… | ………
……… | ……… | Type 252 | 003F0H
Type 29 |  | Type 253 | 003F4H
Type 30 | 00078H | Type 254 | 003F8H
Type 31 | 0007CH | Type 255 | 003FCH