## Slide 1
Presented by
Mahbubur Rahman
Lecturer
Department of Computer Science and Engineering(CSE)
Green University of Bangladesh(GUB)

## Slide 2: 8086 Memory Interfacing
8086 has 20 bits address line.
So, 2^20 = 1MB Memory.
00000 H
FFFFF H
RAM
ROM

## Slide 3
Interface two 4KX8 EPROM and two 4KX8 RAM chips with 8086.
Solution:
Capacity of 2 Chips = 4K X 8 X 2 = 8K X 8 = 8KB
Consider, EA of ROM = FFFFF H
Size = 8KB = 8 X 1KB = 2^3 X 2^10 = 2^13
0000 0001 1111 1111 1111 = 01FFF H So, SA of ROM = FFFFF H – 01FFF H = FE000 H
Consider, SA of RAM = 00000 H Now, 4KB = 2^2X2^10 = 2^12
So, Address Lines = A1 – A12
Ao = Bank Selection (Even/Odd)

## Slide 4
The 8086 microprocessor uses a 20-bit address to access memory. With 20-bit address the processor can generate 220 = 1 Mega address. The basic memory word size of the memories used in the 8086 system is 8-bit or 1-byte (i.e., in one memory location an 8-bit binary information can be stored). Hence, the physical memory space of the 8086 is 1Mb (1 Mega- byte).
For the programmer, the 8086 memory address space is a sequence of one mega-byte in which one location stores an 8-bit binary code/data and two consecutive locations store 16-bit binary code/data. But physically (i.e., in the hardware), the 1Mb memory space is divided into two banks of 512kb (512kb + 512kb = 1Mb). The two memory banks are called Even (or Lower) bank and Odd (or Upper) bank.
The 8086-based system will have two sets of memory IC's. One set for even bank and another set for odd bank. The data lines D0-D7 are connected to even bank and the data lines D8 -D15 are connected to odd bank. The even memory bank is selected by the address line Ao and the odd memory bank is selected by the control signal BHE. The memory banks are selected when these signals are low(active low). Any memory location in the memory bank is selected by the address line A1 to A19.

## Slide 5
 |  | A19 | A18 | A17 | A16 | A15 | A14 | A13 | A12 | A11 | A10 | A9 | A8 | A7 | A6 | A5 | A4 | A3 | A2 | A1 | A0
RAM1 | SA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | EA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
RAM2 | SA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
 | EA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
ROM1 | SA | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | EA | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
ROM2 | SA | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
 | EA | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Memory |  | SA | EA
RAM1 | Even (Lower) Bank | 00000 H | 01FFE H
RAM2 | Odd (Higher) Bank | 00001 H | 01FFF H
ROM1 | Even (Lower) Bank | FE000 H | FFFFE H
ROM2 | Odd (Higher) Bank | FE001 H | FFFFF H